## Slide 1: EE123 Final Project – Image Communication
Lev Tauz, Harrison Wang, Shane Barratt

## Slide 2: JPEG
Color Space Transform
Quantizes 2D DCT coefficients over 8x8 image blocks by point-wise dividing by 3 8x8 matrices and rounding (q in [1, 100] determines quality)
Source: http://www.ams.org/samplings/feature-column/fcarc-image-compression

## Slide 3: Our Implementation in Action
Original – 1.5MB
PSNR = 11.13
Size = 3kB
PSNR = 24.01
Size = 15kB
PSNR = 30.36
Size = 65kB

## Slide 4: Lossless Compression
Gzip

## Slide 5: Packets

## Slide 6: Network

## Slide 7: Physical Layer
Looked into Multiple Frequency Shift Keying (MFSK)
Went with Minimum Shift Keying (MSK) for simplicity
FM Bandwidth is only 3kHz
Went with mark_f = 1200 HZ, space_f = 2400 Hz and baud rate = 2400
Each bit encoded as half sinusoid (mark) or full sinusoid (space) as a result of having the mark and space frequencies divide the baud rate
Frequency Response of the radio’s audio bandpass filter

## Slide 9: Modified Demodulator (no pun intended)
2400
900-2700 Hz
1400
2400Hz

## Slide 10: Results and BER
We’ve doubled the baud rate and thus the amount of bits we can send in the time period
However, how much more likely is it for the transmission to fail and how does this affect our entire system?